## Slide 1: 5DH & EPT2020 DCDC – RFQ
Tobias Grote, Mario Schroeder, Peter Karabinos
CW1740

## Slide 2
Electrical Requirements
Power:
  2200W @60C (160A at 14V on the output)
  1680W @65C (120A at 14V on the output)
Output Voltage:
  Range: 7.5...16V
  nominal: 14V
Efficiency:
  90% @ 11% Pnom
  95% @ 33% Pnom
  91% @ 66% Pnom
  90% @ 100% Pnom
Input Voltage - two HW variants:
  DCDC_HEV: 140V…285V (112V..296V) Vnom: 225V
  DCDC_PHEV: 240V…420V (200V..430V) Vnom : 345V
High speed CAN interface: 500kbps
Overvoltage, Overcurrent, Reverse Polarity Protections
Overheating Protection
Self Diagnostics
Mechanical Requirements
Dimensions: <310mm x 185mm x 34mm
Weight: < 2.5kg
Volume: <1.9 liter
Cooling
  Water cooling
Operating Temperature:
  -30°C – +85°C (ambient)
  -30°C – +65°C (coolant)
Storage Temperature:
  -40°C – 100°C
Tightness: IP67 + IPx9K
Pressure drop: 40mBar@50°C & 8l/min flowrate
5DH DCDC main requirements

## Slide 3
Electrical design

## Slide 4
Converter Topology
Boost converter + LLC half bridge resonant converter
5DH & EPT DCDC160
Diode rectification
Covers wide in-/output voltage range  One DCDC for HEV and PHEV is feasible (5DH)
Low EMI

## Slide 5
DCDC with diode rectifier
Detailed Block Diagram

## Slide 6
Chart: 
| 11% Load Iout=17,6A | 33% Load Iout=52,8A | 66% Load Iout=105,6A | 100% Load Iout=160A
Efficiency Requirement | 90 | 95 | 91 | 90
Expected Efficiency PHEV | 87.293 | 92.0429 | 92.1962 | 91.3142
Expected Efficiency HEV | 86.8439 | 91.863 | 92.0731 | 91.2064
Conditions (5DH)
Vin_PHEV = 345V
Vin_HEV = 225V
Vout = 14V
Efficiency
6
Efficiency curves
Efficiency [%]

## Slide 7
Mechanical design

## Slide 8: Mechanical design
310mm
185mm
34 mm
Housing dimensions:
L x W x H (mm) : 310x225x34 (w/o connectors)
L x W x H (mm) : 310x185x34 (w/o connectors & input wiring section)
Volume : 1.9 l

## Slide 9: Mechanical design 5DH
POWER & CONTROL
BOARD
OUTPUT CONNECTOR
HV & SIGNAL WIRES INPUT
INPUT EMI FILTER
OUTPUT BUSBAR
FIPG SEALING SURFACE
OUTPUT EMI FILTER
WATER COOLING INLET
WATER COOLING
OUTLET

## Slide 10: Mechanical design 5DH
TO247 BONDED WITH
BONDPLY INSULATOR
TO220 BONDED WITH
BONDPLY INSULATOR
MAGNETICS POTTED
IN CHASSIS

## Slide 11
Technical Compliance EMC

## Slide 12
EMC
EMC measures:
Two stage input EMI filter
Two stage output EMI filter
Mechanical shielding
Boost converter comprises good input EMC due to inductor on input side
LLC converter comprises good EMC due to sinusoidal waveforms and varying switching frequency
 Low EMI
 Proposed converter topology + input & output EMI Filter + shielding exhibit good EMC.

## Slide 13
EMC
Switching Frequencies:
New!

## Slide 14
EMC
Input filter parameter:
5DH HEV and EPT 250A have similar max. input current
5DH PHEV and EPT 160A have similar max. input current
For similar input current filter components with equal current rating could be used
 | Vin_min | Pout_max | Iin_max*
5DH HEV | 140 V | 2240 W | 17.8A
5DH PHEV | 240 V | 2240 W | 10.4 A
EPT 160A | 240 V | 2400 W | 11.1 A
EPT 250A | 240 V | 3750 W | 17.4A
* Calculated with 90% efficiency

## Slide 15
Technical Compliance Electrical & functional safety

## Slide 16
Functional safety – OV Management
Over Voltage (OV) Management
Can Delta show that the voltage reference and supply is independent for the both ways of OV detection
2 separate voltage divider for 2 independent measurements
2 separate reference voltages for SW and HW OVP
2 separate ADCs on MCU used

## Slide 17
Technical Compliance

## Slide 18
Measurements
Signal | Symbol | Purpose | Accuracy*
Input voltage | Vin | UV & OV detection | ±0.5%
Input current | Iin | Output current calculation, boost ctrl. | ±1%
DC link voltage | VDC_link | Boost ctrl., power management | ±1%
LLC current | ILLC_prim | OC protection | ±2%
Output voltage | Vout1 | UV & OV protection, regulation | ±1%
Output voltage | Vout2 | Redundant UV & OV protection | ±1%
 Output current is calculated. Expected accuracy: ±2.5% of full scale (200A  ±5A).
*Estimated accuracy of full scale

## Slide 19
Accuracy
Input power accuracy
Requirement:
[TSENS-50]b | DCDC shall provide the input power consumption on DCDC with accuracy better than 0.1 Kw and with resolution 100W
Calculation of input power: Pin = Vin * Iin
Tolerance: (Vin ±0.5%) * (Iin ±1%) = Pin ±1.5%
Worst case example: (250V ±1.25V) * (10A ±0.1A) = 2500W ±37,625W
37,625W much better than required 100W
It’s clear for Delta that input current requirement is removed from TS, the requirement is Input Power.
Output current accuracy
Delta proposal: ±2.5% of full scale (200A  ±5A)
Calculation of output current: η*Pin / Vout = Iout (η: identified efficiency stored in LUT with ±0.5% tolerance)
Worst case example: (90% ±0.45%) * (2500W ±37,625W) * (14V ±0.14V) = 160.7A ±4,89A
±4,89A below the proposel ±5A
Output voltage accuracy
Measurement via voltage divider.
Initial calibration of Vout measurement. Estimated accuracy: ±1%
Worst case example: 25V * ±1% = ± 250mV
± 250mV better than required ±300mV
Yes, Delta confirms that accuracy +/- 300 mV will be reached

## Slide 20
 |  |  |  |  |  | Vout [V] |  |  |  |  |  | 
 | 7 | 7,5 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
190 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
200 | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
210 | 0 | 115 | 115 | 115 | 115 | 115 | 115 | 115 | 115 | 115 | 115 | 0
220 | 0 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 0
230 | 0 | 145 | 145 | 145 | 145 | 145 | 145 | 145 | 145 | 145 | 145 | 0
240 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
250 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
260 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
270 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
280 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
290 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
300 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
310 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
320 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
330 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
340 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
350 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
360 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
370 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
380 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
390 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
400 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
410 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
420 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
430 | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
440 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Operation Range
Vin [V]
Imax available
Pmax available
Dearating
Out of range
Voltage Map for 5DH PHEV
Table: Available output current in A for input and output voltage range

## Slide 21
 |  |  |  |  |  | Vout [V] |  |  |  |  |  | 
 | 7 | 7,5 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
112 | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
120 | 0 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 0
130 | 0 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 0
140 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
150 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
160 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
170 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
180 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
190 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
200 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
210 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
220 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
225 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
230 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
240 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
250 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
260 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
270 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
280 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
285 | 0 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 150 | 140 | 0
290 | 0 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 130 | 0
296 | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
300 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Operation Range
Vin [V]
Imax available
Pmax available
Dearating
Out of range
Voltage Map for 5DH HEV
Table: Available output current in A for input and output voltage range

## Slide 22
Thermal Derating Strategy
+70°C
+65°C
+60°C
Derating regarding specification 5DH:  100% output current / power below +60°C  75% output current / power at +65°C  0% output current / power above +70°C  linear interpolation between this operating points
Temperatures are coolant temperatures.

## Slide 23
Converter Control

## Slide 24
LLC Ctrl.
Structure
xxxx

## Slide 25: Smarter. Greener. Together.