## Slide 1: [Renault 5DH-step1M Sweet400]
Reprog issue on PIE

## Slide 2: Reprogramming Issue
Serial Signature vs Devel Signature Issuevara

## Slide 3: Problem description
FBL_23.19.00.bin  Serial Key
FBL_23.19.00.pdx  Devel Signature
SW_23.15.00.bin  Serial Key
SW_23.15.00.pdx  Serial Signature
FBL_23.19.00.bin  Serial Key
FBL_23.19.00.pdx  Devel Signature
Selfcheck NOK  Application is erased
Selfcheck OK
Flashing completed OK
Flashing completed OK
In addition to the Key used in the SW and FBL, there is also a Signature that is used on the file itself (.pdx) which needs to match in order for the flashing operation to be successful.
1. When the Key is NOK  the unit cannot be unlocked
2. When Signature is NOK  flashing with fail at DTC checking (last step); the app will be invalided and erased
On the parts from PIE, the FBL was not signed with the official Serial Signature  one of the FBL Updaters provided by use was not properly Signed
In order to fix the issue, a new SW was provided with the Development Signature (but Serial Key)
SW_23.15.00.bin  Serial Key
SW_23.15.00.pdx  Devel Signature

## Slide 4: SW Key vs Signature
FBL_23.19.00.bin  Serial Key
FBL_23.19.00.pdx  Serial Signature
FBL_23.19.00.bin  Serial Key
FBL_Updater_231901_to_231900.pdx  Devel Signature
FBL_23.19.00.bin  Serial Key
FBL_Updater_231901_to_231900.pdx  Serial Signature
FBL_23.19.00.bin  Serial Key
FBL_Updater_230698_to_231900.pdx  Serial Signature
FBL_23.19.00.bin  Serial Key
FBL_Updater_202700_to_231900.pdx  Serial Signature
selfcheck
Sharepoint
Provided by HSM Server on Delta Side
Email
SW_23.15.00.bin  Serial Key
SW_23.15.00.pdx  Serial Signature
AVL Team

## Slide 5: Temporary solution
Provided SW_23.15.00 with Serial Key and Development Signature to match the FBL
We study the possibility of providing an updater from FBL_23.19.00 with Development Signature to FBL_23.19.00 with Serial Signature.
The 63 unit reflashed in Cleon are not affected by this issue
Production is not affected by this issue as they don’t use FBL Updaters

## Slide 6: Smarter. Greener. Together.