## Slide 1: Standard Template for Problem Analysis

## Slide 2: Agenda
Problem Description
Open Tasks & Tests
System Architecture
Analysis
Rootcause Description
Solution

## Slide 3: Problem Description
Short Problem Description:
  While in the pentration test, we have found a critical vulnerability where we managed to extract the entire firmware including the bootloader and execute commands on the device .

## Slide 4: Open Tasks & Tests
Task & Tests | Status | Due date | Responsible
Firmware release Version 23.39.94 | Done | WK3 | Bug fix (NRC Update) and Protection in supplier session
Firmware release Version 23.39.93 | In Progress | WK10.5 | Internal release : XCP Protection / or Removal
V&V for Firmware release Version 23.39.93 | Open | WK11 | Validation and Verification for the implementation
Firmware release Version 23.39.92 | Open | WK12 | Release to the customer

## Slide 5: System Architecture
5DH
Client
HV Battery
LV Battery
CAN BUS

## Slide 6: Communication Level
XCP Client
HV COntroller
LV COntroller
CAN BUS: XCP
UART:
XCP:Server

## Slide 7: Analysis: XCP Connection
Tried fetching the data through XCP protocol , to chek the accessability protection.
Result:
The address were accessable with-out any security concern.

## Slide 8: Rootcause
The XCP protocol access on top of the CAN communication layer was not disabled.
XCP protocol was not protected with any security in any of the sessions.

## Slide 9: Solution
OPtion1:
  Add a security layer protection to access the XCP protocol,preferably a customer key protection for the same.
Option2:
  Remove the XCP protocol support from the system.

## Slide 10: Smarter. Greener. Together.