## Slide 1: XCP Issue Fix

## Slide 2: XCP Deactivation
XCP is deactivated by default
XCP access is deactivated from ECUEXT_vMain

## Slide 4: To Activate XCP
DID D008 Delta_Internal_XCP_Activation Write
This DID is available only in Delta Session(Protected by Secure Access)
To Enable XCP : Write 0xAA( Function Enabled ) using 0x2E service
XCP status can be Read using DID D008 Delta_Internal_XCP_Activation
Read
Read the XCP status using 0x22 Service
    0xAA - Function Enabled
    0x00 - Function Disabled

## Slide 6
Need Testing on how long before calling the XCP_Deactivate() , the XCP is active
Basic Developmental Test Done
Testing from the QTS required to fully verify

## Slide 7: Smarter. Greener. Together.