## Slide 1: ADC Peripheral and Configuration
R&D BLR

## Slide 2: SAR ADC Block Diagram
SAR ADC

## Slide 3: 10-bit A/D Block Diagram
ADC Resolution:
2^n - 1

## Slide 4: A/D module Registers
The A/D module has four registers.
A/D Control Register0 (ADCON0)
A/D Control Register1 (ADCON1)
A/D Result High Register (ADRESH)
A/D Result Low Register (ADRESL)
Special Function Registers (SFRs)
  Data register
  Control register
  Status register

## Slide 5: Control Register (ADCON0)

## Slide 6: Control Register (ADCON1)

## Slide 7: A/D Result Register (ADRESH:ADRESL)
The ADRESH:ADRESL registers contains the 10-bit result of the A/D conversion.
When the A/D conversion is complete, the result is loaded into this A/D result register pair, the GO/DONE bit (ADCON0) is cleared.

## Slide 8: A/D Conversion Operation
Steps for doing an A/D conversion:
Configure the A/D module:
  Configure analog pins / voltage reference/ and digital I/O (ADCON1)
  Select the A/D Conversion Clock
  Select A/D input channel (ADCON0)
  Select A/D conversion clock (ADCON0)
  Turn on A/D module (ADCON0)
Wait the required acquisition time.
Start conversion:
    Set the GO/ DONE bit (ADCON0)
Wait for A/D conversion to complete
Read A/D result register pair (ADRESH:ADRESL)
For the next conversion, go to step 1 or step 2, as required.

## Slide 9: Requirements for ADC
Configure Port RA0/AN0 : Pin 2 of PIC as analog input PIN.
Use ADC internal clock as source.
Right justify the ADC Results.
Use Port B and Port C to output the ADC Results.
Use DAC for converting Port Output to Voltage.

## Slide 10: Program
#include <xc.h>
void main(void)
{
  ADCON0=0xC1;
  ADCON1=0x80;
  PORTB=0;
  TRISB=0;
  TRISC=0;
  TRISA0=1;
  ADCON0=(ADCON0|(0b00000100));
while(1)
{
while(ADCON0 &(0b00000100))
{ }
PORTB = ADRESL;
PORTC= ADRESH & 0b00000011;
ADCON0=(ADCON0|(0b00000100));
}
}

## Slide 11: Port A GPIO registers
Configuring Port Pins
Setting a TRISA bit (= 1) will make the corresponding PORTA pin an input

## Slide 12: Port B & C – GPIO registers
Configuring Port Pins
Setting a TRISB/C bit (= 1) will make the corresponding PORTB/C pin an input