## Slide 1: KT Report

## Slide 2: SVN
SVN (Subversion) is a version control system used for managing and tracking changes to files and directories.
It allows multiple developers to work on the same set of files concurrently and keeps track of all changes made to the files.
With SVN, developers can check out a copy of a project from a central repository onto their local machines.
They can make modifications to the files, add new files, and remove existing files. Subversion keeps track of these changes and allows users to commit them back to the repository.

## Slide 3: SVN Basic Features
Tortoise SVN is the graphical client we use for SVN.
  SVN Repository Browser
  SVN Checkout
  SVN Update
  SVN Commit
  Show logs
  Check for Modifications
  Update to Revision
  Revert
  Get Lock
  Add
  Diff

## Slide 4: Building make file
Building a file refers to compiling the Source file by linking all the object and linker files using the specified compiler. The process gives an executable file which can be flashed onto ECU.
A makefile is a special file used to automate the building and compilation process.
  It contains instructions that specify how to build and link the components of a project, such as source code files, libraries, and executables.

## Slide 5: How to Build
> Create S Drive.
> In 20_Make open m.bat file using Notepad++ and add the username and path for the compiler.
>Delete files in Bin
>Open command prompt from Make folder
>m build
Note: In order to standardize the path of files as many developers are involved in the project we use S drive.

## Slide 6: Flashing
Flashing code into an ECU refers to the process of writing or updating the software that controls the functions and behavior of the ECU.
The code is usually flashed into Flash Memory of the Microcontroller.
Connections:
Winidea Debugger is connected to ECU through JTAG and to computer through USB
CAN is connected to computer through USB and to ECU through connector.
Software used: Winidea debugger , CANoe tool

## Slide 7
In an ECU we need to Flash
1)Bootloader
2)Application
The bootloader in an ECU is a software component that facilitates the firmware update process for the ECU.
It allows for the installation of new or updated firmware onto the ECU, which can include improved functionality, bug fixes, performance enhancements.
Before flashing the bootloader we need to Mass erase the flash memory(p and d flashes)

## Slide 8: Process of Flashing
Open .cfg file from CANoe folder in Tools and check for correct channel mapping
Open .xjrf file from winidea folder in tools and check for communication between ECU and debugger
Add Proper .elf file to flash
Download and Play in Winidea
Start in CANoe

## Slide 9: pdx File Creation
PDX file format is used for the exchange of software and configuration data between different tools and systems within the AUTOSAR development workflow.
Hex files are updated and combined using generate bat file.
The combined hex file is given as input to a script ,to produce RSA and CRC file
The newly created 256 byte RSA Key is used to sign the pdx file
The key is replaced in the Helper file and new pdx file is generated.

## Slide 10
Here most part of digital signing is taken care by HEX view software, which is internally called in the generate SHA file. We just need to update the RSA key into helper file and generate the pdx.
Here we are using generate bat file 2 times as the script for creating combined hex file and pdx file is in the same generate bat file. So when we generate combined hex file the script continues to produce a pdx file also which is not the actual updated one with new sign.

## Slide 11: vflashpack
Vflashpack is given to testing team or customer to flash the code onto ECU.
Open any of the previous vflashpack file from release folder using vflash software
Configure new hex file and sign it using the new RSA file
Export the file and Save
Make sure that the logical block index is 0XFD00

## Slide 12
We can flash the application into ECU using the vflashpack file
In the vflash software open the vflashpack file and Flash
Make sure that the CAN channel is mapped correctly
Here the flashing happens through the CAN Bus which make use of the CAN box. So while flashing make sure to connect the CAN box tool
In case of flashing through Winidea Software, it takes place through the debugger.

## Slide 13: Release Folder
Create new Release folder with new software version name (Year, Week, patch)
Add the following updated files into the folder
  .vflashpack file
  .pdx file
  .cdd file
  .dbc file
  .rsa
  .crc file
  .hex file (5DH_FF.hex)
Update the file names according to the release versions

## Slide 14: Vector CANdb++ Editor
The CANdb++ Editor allows users to define the structure of the CAN communication network, including the definition of CAN messages, signal descriptions, and network nodes. It also supports the import and export of databases in various formats.
Features
  Database Creation
  Message and Signal Definition
  Node Configuration
  Signal Multiplexing
  Database Validation

## Slide 15: DBC File
DBC (CANdb) file format is used for defining and describing CAN (Controller Area Network) communication networks. DBC stands for "CANdb" (Controller Area Network database).
DBC files contain information about the messages, signals, nodes, and other elements of a CAN network.
Vector CANdb++ Editor is used to Create and Edit DBC files
On opening the DBC file we can see all the information related to CAN. We can access each elements and edit their values.

## Slide 16: Vector CANdela Studio
It is used for creating and managing diagnostic data according to the CANdela format. CANdela is used for describing diagnostic communication between electronic control units (ECUs) and diagnostic testers.
It allows to define diagnostic data, such as diagnostic services, diagnostic parameters, fault memory, and other relevant information. The tool supports the creation and editing of diagnostic specification files in the CANdela format.

## Slide 17: CDD File
A CDD (CANdela Diagnostic Data) file contains diagnostic specifications that define how diagnostic testers and tools communicate with ECUs to perform diagnostic functions. It includes information such as diagnostic services, diagnostic parameters, fault memory, communication protocols, and more
On opening the CDD file we can see different diagnostic specifications in the left window, selecting them opens new window with its attributes.
Both CDD and DBC files are the input files to Configurator

## Slide 18: Smarter. Greener. Together.