## Slide 1: Software Components

## Slide 2: Application Software Component
Introduction
The application layer consists of the specific software components and many applications which perform specific tasks as per instructions.
The AUTOSAR standard specifies the application layer implementation using a “component” concept.
The AUTOSAR application layer consists of three components which are:
  Application software components
  Ports of software components
  Port interfaces
Software Component is not only logic block, it also contains ports, port interfaces, runnable entities, internal behavior, configuration parameters.

## Slide 3
SWC description includes
General characteristics
  Name
  Manufacturer
Communication properties
  P ports
  R ports
  Interfaces
Inner structure (composition)
  Sub-components
  Connections
  Runnable
Required hardware resources
  Processing time
  Scheduling
  Memory

## Slide 4: Types of Software Components
  Atomic Component
  It cannot be further subdivided and can be assigned to only one ECU.
  It implements a part of the application.
    Application Component : Implement the algorithm
    Sensor/Actuator Component : It handles sensor evaluation and actuator control functions. It depends on associated sensor/actuator and independent of ECU mapped to it.
  Composite Component
  It offers a logical interconnection of other components, which could be either atomic or composite. It can be deployed in different ECUs
  Service component
  A service component in AUTOSAR is standardized and uses standardized interfaces to provide services. Direct access to BSW is needed in order to provide these services to other components

## Slide 5
  Calibration parameter component
  To provide values for calibrating all connected components. If all connected components are not located on the same ECU, the calibration parameter component has to be duplicated and placed on every ECU having at least one other component needing it.
  ECU Abstraction component
  When the sensor-actuator component was described above it was mentioned that it interacted with the ECUAL. To be more precise, it provided access to I/O via a client-server P Port on an ECU abstraction component. This ECU-abstraction component has the ability to interact with other BSW.
  Complex device driver component
  It can communicate directly with other BSW and is typically used for applications with critical resource demands.
      Benefits of SWCs:
          Modularity
          Portability
          Scalability
          Interoperability

## Slide 6: Ports
A port belongs to SWC and it act as the interaction point between a two SWC. A port is associated with a port-interface.
Contents: Data elements (Sender/ Receiver) and Operations (Client / Server).
Provided Ports (P port)
Provided Ports are connection points within a SWC that allow it to expose its services, data, or functionality to other SWCs
Required Ports (R port):
Required Ports are connection points within a SWC that enable it to receive services, data, or functionality from other SWCs

## Slide 7: Ports Interfaces
An interface is attached to a port and it describes the data or operations that are provided or required by a SWC via that port. The interface provides a standardized way for components to interact and exchange information.
Types
  Sender Receiver Port Interface
  Client Server Port Interface

## Slide 8: Client Server Port Interface
The server provides services while one or more clients may use its services to carry out tasks.
Contents: Operations
Communication: 1:1 or n:1 (Multiple client to single server)

## Slide 9: Sender Receiver Port Interface
This way of communicating allows one receiver to get information from multiple senders or a sender to send information to an arbitrary number of receivers.
It defines an asynchronous information distribution and allows for a more data-oriented information exchange over the virtual function bus.
Contents: Data Elements
Communication: 1: n or n:1

## Slide 10: Smarter. Greener. Together.